## Slide 1: Statistics of Grain Size Distributions
Sean Donegan
27-750 Texture, Microstructure, and Anisotropy
Monday, April 28, 2014

## Slide 2: Outline
Why grain size distributions?
Statistical considerations of distributions
  The log-normal distribution
  PDFs and CDFs
Theoretical approaches to grain size distributions
  Hillert distribution
  Mullins distribution
Analysis of real microstructures
  Visualizations
    Histograms
    eCDFs
    Probability plots
  Sampling
  Extreme value theory

## Slide 3: Why grain size distributions?
Grain size has a measurable effect on material properties
Hall-Petch:
σy = yield stress
C = constant
D = ‘grain size’
Creep:
ε = strain rate
n = creep exponent
D = ‘grain size’
.
Real grain sizes exhibit dispersion, which leads to a grain size distribution
So why only one ‘grain size’ in the phenomenological relationships?

## Slide 4: Why grain size distributions?
Answer: no one likes to deal with statistics
Another answer: it’s hard
Kurzydlowski attempted to incorporate grain dispersion into Hall-Petch by defining a constant size of grains (CSG) polycrystal
Berbenni extended Kurzydlowski by defining a size-dependant constitutive equation for elasto-viscoplastic behavior
Both these approaches assume log-normal distributions of grains; but are grain size distributions really log-normal?

## Slide 5: Log-normal distribution
The log-normal distribution describes a random variable whose natural logarithm follows the normal distribution. The cumulative distribution function (CDF) of a log-normal distribution is:
The probability density function (PDF) of a log-normal distribution is:

## Slide 6: PDFs and CDFs
The PDF of a random variable defines the probability of that variable taking a particular value (think ‘bell curve’ e.g. normal distribution)
The integral of a PDF along its domain must equal 1 (i.e., if discrete, all probabilities sum to 1)
The CDF of a random variable defines the probability that a value of the variable will be found <= x (think ‘s-curve’)
The CDF can be defined as the integral of the PDF up to x

## Slide 7: Theoretical approaches: Hillert
Hillert derived a limiting grain size distribution based on a presumed growth equation
Assume grain boundary velocity is proportional to the local curvature:
V = velocity
M = mobility
P = pressure
σ = grain boundary energy
ρ = radii of curvature

## Slide 8: Theoretical approaches: Hillert
The rate of change should be equivalent to the integral of the velocity around the grain boundary surface
This allows us to rewrite the velocity as a rate of change for the grain size:
R = circle/sphere equivalent radius
Rcr = critical radius

## Slide 9: Theoretical approaches: Hillert
By the n-6 rule, the rate of change for grain size in 2D becomes:
n = number of sides
But where does n-6 come from? Originally derived by von Neumann for soap froths, extended by Mullins

## Slide 10: n-6 rule
Consider a plane curve r(θ,t)
red = r(θ,t)
blue = polar vector
green = (directed) tangent
k = Mσ

## Slide 11: n-6 rule
Consider a network of rN(θ,t) curves where all vertices terminate at angles of 2π/3; number the sides and vertices of a given curve in the following manner:

## Slide 12: Theoretical approaches: Hillert
Now determine the average number of sides:

## Slide 13: Theoretical approaches: Hillert
Finally, after some calculus, arrive at the growth equation:
u = R/Rcr
γ = 2αMσ(dt/dRcr2)
τ = lnRcr2
M Hillert, Acta Metall., vol. 13 pp. 227-238 (1965)

## Slide 14: Theoretical approaches: Hillert
The goal is now to arrive at a PDF for the limiting grain size distribution. After some (more) calculus:
M Hillert, Acta Metall., vol. 13 pp. 227-238 (1965)
Is it a PDF?
YES!

## Slide 15: Theoretical approaches: Mullins
Mullins derived a more general form for the limiting grain size distribution that can extend up to ∞ (as opposed to just 2)
The distribution requires a function of the number of sides of a grain (s(x)) and a function G(x) that is conceptually describes whether grains of a particular size will grow or shrink:
W.W. Mullins, Acta Mater., vol. 46 pp. 6219-6226 (1998)
x = R/<R>
d = dimensionality
P = PDF
NB: the integration need not be taken to ∞!

## Slide 16: Theoretical approaches: Mullins
Inverting G(x) yields an expression for the PDF:
W.W. Mullins, Acta Mater., vol. 46 pp. 6219-6226 (1998)
Not all G(x) necessarily yield a true PDF!
If s(x) is defined (in 2D) as a linear function of the number of sides, then Mullins is degenerate to Hillert!
There is no (closed-form) analytical solution in 3D since we lack a well-defined n-6 rule in higher dimensions

## Slide 17: Are they log-normal?
Answer: not really… (they fail the standard tests)
They are not really close to real grain size distributions (or simulations) either!
So where do we go from here?

## Slide 18: Visualizing grain size
Histograms provide a way to visualize the PDF
A histogram discretizes the data by separating it into bins (x axis). The y axis is then the total number of data points that fall in each bin

## Slide 19: Visualizing grain size
Empirical CDFs (eCDF) provide a way to visualize the CDF
The eCDF is a step function that jumps by 1/x for each of the x data points
red = actual data
blue = sampled from ideal normal

## Slide 20: Visualizing grain size
Probability plots compare empirical data to a theoretical distribution
Probability plots may have different types of axes (quantiles or probabilities)
The shape of the curve on a probability plot determines the shape of the underlying distribution

## Slide 21: Sampling
Actual problem: how does one sample data points from a given PDF?
One answer: inverse transform sampling
Inverse transform sampling requires knowing the quantile function, which is the inverse of the CDF:
Unfortunately, not all CDFs can be expressed in terms of elementary functions, and thus cannot be inverted (not even the normal distribution); this is the case for the general Mullins, but not for the Hillert

## Slide 22: Numerical CDFs

## Slide 23: Numerical CDFs

## Slide 24: Numerical CDFs
Construct a numerical CDF by computing the cumulative sum of the areas:
A grain size can now be sampled by finding a random (real) number, Q, on the interval [0,1], and comparing it to the set P:

## Slide 25: Extreme value theory
In some material systems, large grains (“as-large-as”, or ALA) play an important role in failure, since they often serve as the nucleation site for fatigue cracks

## Slide 26: Extreme value theory
IN100

## Slide 27: Extreme value theory
Fisher-Tippett-Gnedenko Theorem: The maximum of a random variable converges in distribution to either the Gumbel, Fréchet, or Weibull distribution.
Pickands-Balkema-de Haan Theorem: For some unknown distribution of a random variable, the distribution of values beyond some threshold, u, converges in distribution to the generalized Pareto distribution (GPD).

## Slide 28: Extreme value theory
ξ = shape parameter
σ = scale parameter
μ = location parameter
x
density
ξ+

## Slide 29: Extreme value theory
The tails of different grain size distributions can be quantitatively compared (given suitable normalization)

## Slide 30: Extreme value theory
The shapes of the upper tails of grain size distributions appears correlated to grain growth kinetics: upper tails become longer (more akin to log-normal) as the microstructure stagnates
Analytical approaches to plane curve evolution indicate that the limiting (self-similar) size distribution is uniquely determined by the initial tail distribution
“Analytical approaches” means application of mean curvature flow to a collection of disjoint plane curves